## MODEL 2002 MESSAGEBOARD TRM

Sign Display:

# Height					36”

Length					72”

Width					6”

2 or 3 line capability			8 characters per line

# Standard character pixel format is 5 horizontal by 7 vertical

Character matrix display creating characters or symbols

Pixel clusters contain yellow/amber color

Each pixel cluster is encapsulated in polycarbonate housing

Pixel clusters are sloped at a downward angle of 6 degrees for optimum display viewing

Sign is visible & legible at 750 feet day or night with a photo sensor illuminator

Front opening panels for ease of maintenance

Weatherproof with a positive exhaust fan system

Sign Control:

# Laptop computer IBM standard

Windows based menu driven software control

Truck Mounted System:

Tubular steel construction

Sign display lift mechanism is powered by mechanical lift system.  Sign will lift to upright position for easy placement to traffic flow.  Sign locks in place by a positive locking mechanism.

Manufacturer reserves the right to make changes in its products from time to time without incurring any obligation to incorporate such improvements in any products previously sold or in service.